ACC++ Manual
Everything you could ever want to know about ACS

# Introduction
## Introduction to the Manual
This manual is going to be written as I design and write the ACC++ compiler. My hopes are that the manual will describe anything and everything related to ACS. Although the ACC++ project is primarily focused around utilizing the features of ZDoom, included will be documentation on the original byte code format as well as any other extensions that I may stumble upon.
Seeing that I plan on writing this as I go, the beginning will focus mostly on the byte code of ACS. From there I will describe the features of the ACS and ACS++ languages along with any differences from the implementation of ACC. I will not describe the functionality of each individual action special as they are all processed by the lspec instructions. A good reference for the functionality of these action specials would be the ZDoom wiki.[1] Although I will briefly cover the byte code for each built in instruction I will still expect some external reference for specific details.[2]
[1] Action special reference can be found at the following location: http://zdoom.org/wiki/Action_specials
[2] Reference for the “built in” functions can also be found on the ZDoom wiki: http://zdoom.org/wiki/Built-in_ACS_functions
## Introduction to ACS and ACS++
ACS is a scripting language that was designed by Raven Software for use within Hexen. ACS provides a form of C style scripting which vastly expands the capabilities of the Doom engine. The source to the compiler, ACC, has been released by Raven software under a restrictive license. This code base has been used to create the compiler used by ZDoom. ZDoom uses a greatly expanded version of ACS which can be described as the de facto implementation due to its popularity.
Some of ZDoom's extensions, namely arrays, provided the base for which ACS++ can operate on. Specifically global arrays have no definite bounds, which is a property that will be used by ACC++ to allow a form of pointers, and by extension OOP to be possible. Other features implemented by ZDoom will also play a major role within ACS++, such as functions and libraries.
The ACC++ project was started on June 3rd, 2010 after much anticipation from the Doom community (although planning was started as far back as February of 2010). It is licensed under the 3-clause BSD license in hopes that it can be used in various Doom projects, such as within ZDoom itself. ACC++ is a drop in replacement for ACC and will be backwards compatible with existing implementations of the ACS virtual machine, although certain ZDoom extensions will be needed in order to use the ACS++ language.
As a replacement for ACC, ACC++ does not plan on extending the byte code format where possible, and will not specifically allow anything new to be created. Although the availability of object oriented concepts should make some things that would be otherwise difficult to manage a bit easier. In addition ACC++ will not provide complete compatibility with ACS (think C++ vs. C), but should allow existing code to compile with some minor changes.
# Byte Code
## Data Types and Other Numbers
Before reaching into the detailed specification for the ACS byte code format, we will define our data types. Excepting for strings, all data types will be stored in little endian byte order (least significant first). Strings will be stored as they are seen ending in a '\0' byte unless otherwise noted.
For the purposes of this textbook signed values should be assumed unless otherwise noted. The data type int will be used to represent a 32-bit integer, short for 16-bit, and char for 8-bit (with a string being an array of chars). The type fixed is a 32-bit integer where the upper 16 bits represents a whole value and the lower 16-bits represents a fractional value out of 216.
### Script Types
In order to handle various events on the map scripts are given one of the following types. These will be referred to as ScriptType within this document.
1. CLOSED	A normal script with no special trigger.
2. OPEN	Script that is executed at the start of a game (world). It must be called only once per map, UNLOADING can be used for returns.
3. RESPAWN	Script that is executed by the player on respawn.
4. DEATH	Script that is executed by the player when they are killed.
5. ENTER	Script that is executed by the player when they enter the game. If spectating is supported then this should only be when the player enters the game physically. Should only be executed once per player.
6. PICKUP[*]	Executes whenever a flag (for any team) is picked up in CTF.
  [*] These were defined for Skulltag's capture the flag game modes. They can be considered deprecated.
7. BLUERETURN*	Executed when the blue team's flag is returned in CTF.
8. REDRETURN*	Executed when the red team's flag is returned in CTF.
9. WHITERETURN*	Executed with the white flag is returned in one flag CTF.
              Types 9 through 11 are undefined.
1. LIGHTNING	Executes whenever lightning strikes on the map.
2. UNLOADING	Executed by the world before the level is finished. It should be executed until the first delay, at which point execution may continue only if the level is returned to.
3. DISCONNECT	Should take one argument, which will be filled with the player number of the disconnecting player. Note that in ports that allow spectating this should also happen if the player turns into a spectator.
4. RETURN	Like ENTER, but executed when the player returns to the map.
### Script Flags
In addition to the script type a script may have flags associated which change how the script is executed. Within this document these will be referred to as ScriptFlags.
1. NET	Allows the player to “puke” the script. (That is execute from the console or by button press.)[3]
  [3] At one point in time this flag also implied CLIENTSIDE in Skulltag, however due to incompatibility issues this has been changed to only mean “can be puked.”
2. CLIENTSIDE	Causes the script to be executed by the client in a client server model. This implies that the server does not need to be informed of any changes to the script. Also, any script not carrying this flag is assumed to be server side only.
### Magic Limits
Since ZDoom has changed many of the hard limits I feel it's worth documenting these changes. Here is a table of some of the magic numbers with their old and new values.
Limitation	Hexen	ZDoom
Scripts	64	65535[4]
Map Variables	32	128
Script Variables	10	20[5]
World Variables	64	256
Strings	128	32768
Global Variables	N/A	64
Functions	N/A	256
Translations	N/A	32
[4] ZDoom supports 32767 numbered scripts since r3359, script 0 is reserved for system use, and negative scripts are used for named scripts. Before this only 1000 scripts were supported.
[5] Can be increased with SVCT chunks.

## Variable Scope and Arrays
Due to the various references to scope throughout the byte code documentation it is worth taking some time here to note what each scope means. In general there are 4 scopes in ACS, local, map, world, and global. The last one, global, is an addition by ZDoom, but will be an important role in ACS++.
The local scope is simply all of the variables within a script or function. These are automatically assigned indexes by the compiler. Each script or function should have it's own local scope.
The map scope are those global to a particular behavior lump. It may also include variables pulled in from a library. These, like those in the local scope, are also automatically assigned their indexes. One major difference between map variables and local variables is that map variables can be an array. Exclusive to the map scope arrays is the ability to be initialized during their definition.
The world scope contains variables that are carried over through an entire hub. When not in a hub they are functionally identical to map variables. However due to the ability to be carried over maps they must be manually assigned their index and can not be initialized during definition.
The last scope, introduced by ZDoom, is global. These variables are carried during game play to all maps until a new game starts. These are useful for tracking stats between levels and will be the basis for the memory heap in ACS++. Otherwise they are very similar to world variables.
Some things to note about world and global arrays. First is that they do not share their indexes with world and global variables.[6] ZDoom defines a limit of 256 world variables and arrays, and 64 global variables and arrays. The second important feature is that they world and global arrays have no defined size. An ACS++ conforming VM must have the ability to dynamically resize these arrays.
[6] Technically map arrays and variables are implemented such that they do not share indexes. However the MEXP chunk is used to name both the arrays and variables assuming they are on a shared index.
## Detecting Byte Code Format
As of this writing there are three known byte code formats. The first we'll be covering is the Hexen byte code format, henceforth known as ACS0, which can be identified by the 4-byte header of “ACS\0”. ZDoom introduces two enhanced byte code formats. The first being ACSE, and the latter being ACSe.
Although not required, ZDoom's ACC generally generates an empty ACS0 script at the beginning of the file and thus the detection of the format is not entirely straightforward.
Type	Name	Description
char[4]	Identifier	May be “ACS\0”, “ACSE”, or “ACSe”
int	DirOffset

If the Identifier is ACSE or ACSe our work is done, otherwise we need to check the char[4] at the DirOffset-4. If this is ACSE or ACSe then we need to switch to the respective format. In that case we will need to get our new DirOffset from DirOffset-8.
Note that if a Hexen script isn't faked, then you will need to use the 12 byte version of the SPTR chunk (see ZDoom Enhanced Formats for more details). It is worth noting that it is not believed that were are many (if any at all) scripts which use the 12 byte SPTR.
## ACS0 Script Directory And Byte Code
At DirOffset the first int represents the number of scripts within the lump. The number of scripts is followed by that many pointers. These pointers are in the following format.
Type	Name	Description
int	Number	The actual number is this int mod 1000. This number divided by 1000 will represent the ScriptType.
int	Address	Position in which the script starts.
int	ArgCount	The number of arguments the script takes. Due to limitations this should be no larger than 3.

After the script pointers is an int for the number of strings in the strings table. This will be followed by the same amount of ints referencing the position within the lump at which the string starts. All strings are standard NULL terminated char arrays.
An ACS0 script is relatively straightforward. It consists of an int for the pcode followed by additional ints for any parameters the pcode may take. This is repeated until PCD_TERMINATE is reached. See appendix B for a list of pcodes and their functions.
## ZDoom Enhanced Formats
ZDoom offers two enhanced byte code formats. Both ACSE and the newer ACSe are chunk based. As such the DirOffset from the header now indicates the offset to the start of the chunk data rather than an actual directory. Below is the format of the chunk header.
Type	Name	Description
char[4]	Identifier
int	Size

None of the chunks are required, however some of the chunks can be assumed that there are only one instance of them. In this documentation you may assume that you should only find one of each chunk unless otherwise specified.
The ACSe format uses a more compact byte code format. Instead of the pcode being a full integer, it uses a single byte for codes 0-239. For 240 (256-16) and up, a short is used with the following formula (assume that pcode already contains the first byte).
pcode = 240 + ((pcode - 240)<<8) + nextbyte;
### ARAY, AINI, and AIMP Chunks
The ARAY chunk holds information about the map arrays defined in the script. The number of arrays can be found by dividing the chunk size by 8. The format for each array is an int for the array's number followed by an int for the size of the array.
An AINI chunk initializes one of the arrays defined in the ARAY chunk. There can be as many of these chunks as there are map arrays defined in the ARAY chunk. The format is an int followed by one int for each element in the array as defined in ARAY.
The AIMP chunk is used to list information on the arrays that have been imported from a library. It first has an int for the number of arrays that have been imported which will be followed by one of the following structures for each array. The local number will be a reference to the array in another script by name.
Type	Name	Description
int	Number	Local map variable to assign reference to.
int	Size	Expected size.
char[]	Name	Null terminated string. This string will be looked up in the MEXP chunk.

### ASTR, ATAG, and MSTR Chunks
These chunks are used in libraries to notify of variables and arrays that hold string values. They will have to be tagged at run time with an identifier. This identifier is stored in the upper 16-bits of the string's index just as the tagstring instruction does.
The MSTR chunk is for map variables. The number of variables referenced can be found by dividing the chunk size by 4 and will be followed by that many ints referencing the map variables by their index.
The ASTR chunk does the same for map arrays. Same format is MSTR except the variable index refers to an array. Note that you will have to flag all the strings in the array based on the size found in the AIMP chunk.
A more advanced version of ASTR known as ATAG may also be present. This chunk allows mixed type arrays (structures). Only one array may be present in the chunk, but multiple chunks may exist. The first char of the chunk is the chunk version number which should be 0. The next int is the array number and the following chars are the type of the corresponding array index. The types are 0 – Integer, 1 – String, 2 – Function Pointer. Ending 0s may be truncated so check the chunk size while reading. If this chunk is mixed with the ASTR chunk on the same array, the result is undefined.
### LOAD Chunk
This chunk provides the names of the libraries in which to load. The chunk is simply a list of null terminated strings with each string representing the name of one library. As of this writing these strings should not consist of more than 8 characters each. The only way to determine how many libraries are loaded is by checking to see if the chunk size has been reached.
### FUNC and FNAM Chunks
The FUNC chunk holds information about the various functions that are in the script. The number of functions can be determined by dividing the chunk size by 8. For each function (including imported functions) the following structure is used.
Type	Name	Description
char	NumArgs
char	NumVars
char	HasReturn	Actually a boolean.
char		Always 0.
int	Address	Lump offset to the start of the function's code. 0 is used when importing.

The FNAM chunk is a string table which indexes the names of each function in the lump. For information on the formatting of the string tables see the STRL and STRE chunks documentation.
### MEXP, MINI, and MIMP Chunks
The MINI and MIMP chunks are similar to the array counterparts AINI and AIMP. An MINI chunk initializes the map variables. The format is an int for the index of the first variable and one int for each variable's value. The number of variables initialized can be found by dividing the size of the chunk by 4 and then subtracting 1.
The MIMP chunk is used to list information on the map variables that have been imported from a library. This chunk is just a list of the following structures, so you will need to check against the chunk size to determine the number of variables imported. This chunk makes the map variable index specified a reference to a map variable in another script by name.
Type	Name	Description
int	Number	Local variable to assign reference to.
char[]	Name	Null terminated string.

The MEXP chunk is used in the lump for a library to store string table with the names of the map variables and arrays. See the STRL and STRE chunks for more details.
### SPTR, SFLG, SNAM, and SVCT Chunks
The SFLG chunk is an additional chunk used to define the ScriptFlags for a particular script. The number of scripts referenced can be found by dividing the chunk size by 8. It will be followed by that many of the following structures.
Type	Name	Description
short	ScriptNumber
short	ScriptFlags	See ScriptFlags reference in Data Types and Other Numbers.

The SVCT flag changes the limit on the number of local variables a script can use (the default limit is 20). The format of this chunk is the same as SFLG except the ScriptFlags would represent the number of local variables available.
The SPTR chunk is the replacement for the script directory. There are two possible versions of SPTR. The early version is used if the script lacks the fake Hexen script. For the sake of chronological order, I'll be documenting that version first.
In the early version the number of scripts defined by the SPTR chunk is the chunk size divided by 12. It will be followed by that many of the following structure.
Type	Name	Description
short	ScriptNumber	See below for details.
short	ScriptType	See ScriptType reference in Data Types and Other Numbers.
int	Address	Relative to the entire lump.
int	ArgCount

For the modern version number of script is defined by the size of the chunk divided by 8. This structure is used if the script appears as a normal Hexen script to a non-ZDoom ACS aware VM. The structures will be in the following format.
Type	Name	Description
short	ScriptNumber	See below for details.
char	ScriptType	See ScriptType reference in Data Types and Other Numbers.
char	ArgCount
int	Address	Relative to the entire lump.

ScriptNumber can be negative, in which case it refers to the index of a named script. Valid normal script numbers are 0-32767 although script 0 should be reserved for use by the port. Scripts above 999 may not be supported by all VMs. The name of a named script is stored in the SNAM chunk is a string table which assigns names for each named script from -1 counting down (see STRL and STRE documentation).
### STRL and STRE Chunks
These are the string table chunks. STRL is a normal string table and STRE is an encrypted string table (encryption is enabled through ACC's #encryptstrings option). The format of the standard string tables are an int that is wasted[7], an int for the number of strings in the table, followed by another wasted int. This will be followed by an int for each string in the table which represents the offset to that string in the chunk (note that these will also be part of the keys during encryption).
[7] Seems to have once been used for supporting multiple languages in ACS. When this was the case the field was char[4] identifying the language of the string table (more than one STRL possible), but this is no longer supported and thus should simply be set to 0.
The encryption uses a fairly simple algorithm in which encryption and unencryption is done through the same process. The encryption key is the offset in the chunk to the string multiplied by 157,135. With the key, loop through each character taking the exclusive or of the character with the key+x where x is the character number divided by two.
A note about other string table chunks (FNAM, MEXP, and SNAM), their format does differ slightly in that the two wasted ints do not exist.
Also, strings within the string tables do not have their escape characters removed. This must be done by the VM.
# Assembly
## Introduction to ACS Assembly
ACC++ provides a low level scripting language for ACS scripts. It primarily exists so that internal functions can be easily defined without needing to update ACC++. It also serves as an abstraction layer for the various byte code formats. The assembler does implement some optimizations so the output isn't always one to one with what is specified.
Most users will not need to worry about the assembler as the standard library will provide a wrapper for all of the known ACS functions. However, it could be useful if you are getting runaway scripts and are looking for ways to reduce your instruction count. Ultimately ACS(++) code will be translated into assembly during compilation, so should you decide to take advantage of this feature you will be able to use in-line assembly.
## Mnemonic Definitions
Every instruction in the assembly language is given an unique mnemonic. Mnemonic definitions tell the assembler which instruction the mnemonic represents as well as what parameters it may take. The syntax of a normal mnemonic definition is as follows:
mnemonic number instruction, “parameters”
The number is the pcode for the instruction (see Appendix B for a complete reference). The instruction can be any identifier as long as it has not been previously defined. Note that mnemonic names are not case-sensitive. Each character in the string provided for parameters indicates one parameter that must be provided with the mnemonic. If the first character is '+' then it indicates that the parameters should be 4-byte aligned. Otherwise 'I' is used for 32-bit integers, 'S' for 16-bit integers, or 'B' for an 8-bit integer.
The '-' character may be used after any of the previously mentioned characters to represent that the parameter type is repeated by the value specified in that parameter. For example if “B-” is used then the first parameter would be a byte representing how many bytes should follow.
In addition to normal mnemonics the assembler uses a concept of “const mnemonics.” These are used to link two similar mnemonics together. The normal mnemonic being the one that gets it's values from the stack. If enough constant values are pushed onto the stack before a call to a normal mnemonic then the assembler will remove the pushes and substitute the const mnemonic.
constmnemonic number instruction, normalInstruction, “parameters”
Const mnemonic definitions must always come after the normal mnemonic was defined. Typically the instruction names for const mnemonics are the same as the normal mnemonic with “direct” appended. For example lspec1 becomes lspec1direct.
## Assembly Language
First, it is important to note that ACC++ still uses the ACS preprocessor for ASM code. As such, a typical ASM script will likely start by including the mnemonics.inc file from the standard library. This also means that the ACC++ assembler uses C-style comments.
Writing scripts in assembly is simply a matter of writing the mnemonic you want to call followed by whatever parameters it may take. To ease coding any instruction call in the assembly code can be proceeded by a label. These labels may be used as a parameter for any instruction. The following example code prints the number 65535 to the screen:
#include “mnemonics.inc”
// Syntax will be discussed later.
section scripts
1 CLOSED 0 ExampleCode
ExampleCode:
beginprint
pushnumber 65535
printnumber
endprint
terminate // All scripts should end in a terminate instruction.
## Data Sections
A list of instructions isn't too useful by itself. Various sections are defined in order to provide static data and/or define entry points for scripts and functions.
### Functions
Provided you are not using Hexen compatible scripts, functions can be defined though the functions section.
section functions
Label: argumentCount varCount returns entryPoint, ...
The Label is optional, but is useful for referring to functions by name for the call/calldiscard instructions. The argumentCount specifies how many arguments the function takes and varCount indicates how many variables the function uses. Returns should be 1 (true) or 0 (false). EntryPoint should be the label for the starting instruction. Functions are terminated by the returnvoid or returnval instructions.
### Load
section load
“LIBRARY”, …
Provides a list of library names in which to load. Library names should be no longer than 8 characters.
### Maparrays and Mapvariables
Although Hexen provides the concept of map variables, the static initialization of them is not supported. One thing to note when using these sections is that although the indexes are not necessarily linked, when creating a library the variable names share a common index.
section mapvariables
Label: index { value }, // Or
Label: index { value }:strings, // Or
Label: index varName
Although the label is optional, it is used in libraries to allow other scripts to reference the variable. The first form initializes the variable to an integer. The second form initializes the variable to a string. The third form is used if you want to import the variable from a library.
section maparrays
Label: index size { values, ... }, // Or
Label: index size { values, ... }:strings, // Or
Label: index size varName
Handles the initialization of map arrays. When initializing to values (not importing) you must specify the same number of values as you specified for the size.
### Scripts
The scripts chunk defines the entry points of scripts as well as how it should be executed. Note that the optional portions of the following syntax are not available when compiling Hexen compatible scripts.
section scripts
number type argumentCount entryPoint, // Or
number type argumentCount entryPoint[varCount], // Or
number type argumentCount entryPoint flags..., // Or
number type argumentCount entryPoint[varCount] flags..., // Or
name type argumentCount entryPoint[varCount] flags
The number is of course number in which you wish to reference the script as within the maps. The type can be any of the values defined in ScriptType. The argumentCount is how many arguments the script can take. This can be any number between 0 and 3 inclusive. The entryPoint is the label for the first instruction in the script. If you are not using Hexen compatible scripts you can additionally provide a varCount to increase the number of script variables available from 20 (or 10 in the case of Hexen scripts). Flags can be any number of the ScriptFlags values. Named scripts are also unsupported in Hexen format.
### Strings
section strings
Label: “String”, …
Provides a list of strings in which to put into the string table. The label is optional, however, it does allow you to reference strings by name rather than by index.
# Appendix A: Script Optimizations
## Solving Runaway Scripts
At least in ZDoom, an instruction limit is imposed for every tic. This limit is 2,000,000 (used to be 500,000) instructions. In general you should not reach this limit, however if you do here are a few tips on how to avoid it. Keep in mind that most of the time when this limit is reached it is because of loops or recursive functions. Therefor even if it may seem like these techniques only save an instruction or two you might end up saving more than you think.
### Avoid Providing Optional Arguments
Whenever possible you should avoid providing the optional arguments. Unless you are using a constant expression, each argument produces at least one push instruction which counts towards your limit. For example, if you use the ACS_Execute function and you don't need to pass in any arguments only provide the fist two. See the following code:
#include “zcommon.acs”
script 1 (void)
{
// This call will use 5 push instructions followed by an lspec5.
ACS_Execute(2, 0, 0, 0, 0);
// This functionally identical call will use 2 push instructions and lspec2.
ACS_Execute(2, 0);
}
### Use “const:” Where Possible
Probably the simplest thing to do provided none of your arguments are expressions. Simply place “const:” before the first argument on your action special calls and avoid using push instructions completely. Observe the following:
#include “zcommon.acs”
script 1 (void)
{
// 6 instructions
ACS_Execute(2, 0, 0, 0, 0);
// 1 instruction
ACS_Execute(const:2, 0, 0, 0, 0);
}
In addition to all line specials, you can use const on any of the following functions: Delay, Random, ThingCount, TagWait, PolyWait, ChangeFloor, ChangeCeiling, ScriptWait, SetGravity, SetAirControl, GiveInventory, TakeInventory, CheckInventory, Spawn, SpawnSpot, SetMusic, LocalSetMusic, and SetFont.
This can not be combined with leaving out optional arguments for the purposes of saving “cycles,” however you may do so in order to save space on the compiled byte code.
# Appendix B: PCode Reference
## PCode Table
In all there are 353 defined PCodes. The extension column states what engine introduced the PCode. Required indicates if it is needed for ACS++. In addition all Hexen PCodes are listed as required. “St. Of.” (stack offset) indicates the expected shift in stack size. The codes highlighted in gray are named however are not, and to my knowledge never have been, defined programmatically.
For most functions I'll just say “See FunctionName(<num parameters>[, <max parameters>]).” The number of parameters is a constant in the byte code, so the number of optional parameters is merely provided here for reference purposes. To learn more about these functions I recommend checking out the page on the ZDoom wiki. (http://zdoom.org/wiki/Built-in_ACS_functions)
It is important to note that for function calls in ACS, the first item pushed onto the stack is the first argument, the next would be the second argument and so forth. Likewise when performing operations the first item pushed onto the stack is the operand to the left of the operator and the second item would be the right operand. That said when I describe which stack item to use for what I will be using “1st” to mean the top of the stack and not the first item pushed.
Note: For ACSe, all variable indexes (including array numbers) are chars instead of ints.
#	PCode	Args	St.Of.	Ext	Req	Description
0	nop	0	0	Hexen	X	Does nothing
1	terminate	0	0	Hexen	X	Finishes the current script.
2	suspend	0	0	Hexen	X	Holds the execution of the script until it is executed again, at which point it will resume.
3	pushnumber	1	1	Hexen	X	Pushes an int onto the stack.
4	lspec1	1	-1	Hexen	X	Executes the line special using removing one argument from the stack.
5	lspec2	1	-2	Hexen	X	Same as lspec1 only uses 2 args from the stack.
6	lspec3	1	-3	Hexen	X	Same as lspec1 only uses 3 args from the stack.
7	lspec4	1	-4	Hexen	X	Same as lspec1 only uses 4 args from the stack.
8	lspec5	1	-5	Hexen	X	Same as lspec1 only uses 5 args from the stack.
9	lspec1direct	2	0	Hexen	X	Executes the line special in the first arg (char in ACSe) with one constant parameter (int).
10	lspec2direct	3	0	Hexen	X	Same as lspec1direct only with 2 arguments.
11	lspec3direct	4	0	Hexen	X	Same as lspec1direct only with 3 arguments.
12	lspec4direct	5	0	Hexen	X	Same as lspec1direct only with 4 arguments.
13	lspec5direct	6	0	Hexen	X	Same as lspec1direct only with 5 arguments.
14	add	0	-1	Hexen	X	Adds the last two items from the stack, pushing the result.
15	subtract	0	-1	Hexen	X	Subtracts the last two items from the stack pushing the result.
16	multiply	0	-1	Hexen	X	Multiplies the last two items from the stack pushing the result.
17	divide	0	-1	Hexen	X	Divides the last two items from the stack pushing the result. Errors on division by zero.
18	modulus	0	-1	Hexen	X	Calculates the remainder of division of the last two items on the stack, pushing the result. Errors on modulus by zero.
19	eq	0	-1	Hexen	X	Pushes 1 to the stack if the last two items are equivalent, otherwise pushes 0.
20	ne	0	-1	Hexen	X	Pushes 1 to the stack if the last two items are not equivalent, otherwise pushes 0.
21	lt	0	-1	Hexen	X	Pushes 1 to the stack if the 2nd item in the stack is less than the 1st, otherwise pushes 0.
22	gt	0	-1	Hexen	X	Pushes 1 to the stack if the 2nd item in the stack is greater than the 1st, otherwise pushes 0.
23	le	0	-1	Hexen	X	Pushes 1 to the stack if the 2nd item in the stack is less or equal to the 1st, otherwise pushes 0.
24	ge	0	-1	Hexen	X	Pushes 1 to the stack if the 2nd item in the stack is greater than or equal to 1st, otherwise pushes 0.
25	assignscriptvar	1	-1	Hexen	X	Assigns the value on the stack to the specified local variable.
26	assignmapvar	1	-1	Hexen	X	Assigns the value on the stack to the specified map variable.
27	assignworldvar	1	-1	Hexen	X	Assigns the value on the stack to the specified world variable.
28	pushscriptvar	1	1	Hexen	X	Pushes the value of the local variable onto the stack.
29	pushmapvar	1	1	Hexen	X	Pushes the value of the map variable onto the stack.
30	pushworldvar	1	1	Hexen	X	Pushes the value of the world variable onto the stack.
31	addscriptvar	1	-1	Hexen	X	Adds the stack to the specified local variable.
32	addmapvar	1	-1	Hexen	X	Adds the stack to the specified map variable.
33	addworldvar	1	-1	Hexen	X	Adds the stack to the specified world variable.
34	subscriptvar	1	-1	Hexen	X	Subtracts the stack from the specified local variable.
35	submapvar	1	-1	Hexen	X	Subtracts the stack from the specified map variable.
36	subworldvar	1	-1	Hexen	X	Subtracts the stack from the specified world variable.
37	mulscriptvar	1	-1	Hexen	X	Multiplies the stack to the specified local variable.
38	mulmapvar	1	-1	Hexen	X	Multiplies the stack to the specified map variable.
39	mulworldvar	1	-1	Hexen	X	Multiplies the stack to the specified world variable.
40	divscriptvar	1	-1	Hexen	X	Divides the stack from the specified local variable. Errors on division by zero.
41	divmapvar	1	-1	Hexen	X	Divides the stack from the specified map variable. Errors on division by zero.
42	divworldvar	1	-1	Hexen	X	Divides the stack from the specified world variable. Errors on division by zero.
43	modscriptvar	1	-1	Hexen	X	Takes modulus of the local variable by the stack.
44	modmapvar	1	-1	Hexen	X	Takes modulus of the map variable by the stack.
45	modworldvar	1	-1	Hexen	X	Takes modulus of the world variable by the stack.
46	incscriptvar	1	0	Hexen	X	Increments the local variable by one.
47	incmapvar	1	0	Hexen	X	Increments the map variable by one.
48	incworldvar	1	0	Hexen	X	Increments the world variable by one.
49	decscriptvar	1	0	Hexen	X	Decrements the local variable by one.
50	decmapvar	1	0	Hexen	X	Decrements the map variable by one.
51	decworldvar	1	0	Hexen	X	Decrements the world variable by one.
52	goto	1	0	Hexen	X	Sets the script execution to the offset specified.
53	ifgoto	1	-1	Hexen	X	Same as goto except it first checks to see if the stack doesn't equal zero.
54	drop	0	-1	Hexen	X	Removes one value from the stack.[8]
55	delay	0	-1	Hexen	X	Causes the script to wait for the number of tics specified on the stack. See also Delay(2).
56	delaydirect	1	0	Hexen	X	Same as delay only with constant parameters.
57	random	0	-1	Hexen	X	Picks a random number inclusively between the last two items on the stack. See also Random(2).
58	randomdirect	2	1	Hexen	X	Same as random only uses constant parameters.
59	thingcount	0	-1	Hexen	X	See ThingCount(2)
60	thingcountdirect	2	1	Hexen	X	Same as thingcount, uses constant parameters.
61	tagwait	0	-1	Hexen	X	Waits for the tag in the stack to finish moving. See also TagWait(1).
62	tagwaitdirect	1	0	Hexen	X	Same as tagwait, uses constant parameters.
63	polywait	0	-1	Hexen	X	Waits for the polyobj number in the stack to finish moving. See PolyWait(1).
64	polywaitdirect	1	0	Hexen	X	Same as polywait, uses constant parameters.
65	changefloor	0	-2	Hexen	X	See ChangeFloor(2).
66	changefloordirect	2	0	Hexen	X	Same as changefloor, uses constant parameters.
67	changeceiling	0	-2	Hexen	X	See ChangeCeiling(2).
68	changeceilingdirect	2	0	Hexen	X	Same as changeceiling, uses constant parameters.
69	restart	0	0	Hexen	X	Sets the script execution offset back to the beginning of the script.
70	andlogical	0	-1	Hexen	X	Pushes 1 if the last two items on the stack are true, otherwise pushes 0.
71	orlogical	0	-1	Hexen	X	Pushes 1 if either of the last two items on the stack are true, otherwise pushes 0.
72	andbitwise	0	-1	Hexen	X	Performs a bitwise and operation on the last two items on the stack, pushing the result.
73	orbitwise	0	-1	Hexen	X	Performs a bitwise or optionation on the last two items on the stack, pushing the result.
74	eorbitwise	0	-1	Hexen	X	Performs a bitwise exclusive or optionation on the last two items on the stack, pushing the result.
75	negatelogical	0	0	Hexen	X	Switches the last item on the stack from true to false or vice versa.
76	lshift	0	-1	Hexen	X	Performs a left shift operation on the last two items on the stack, pushing the result.
77	rshift	0	-1	Hexen	X	Performs a right shift operation on the last two items on the stack, pushing the result.
78	unaryminus	0	0	Hexen	X	Changes the last item on the stack from positive to negative or vice versa.
79	ifnotgoto	1	-1	Hexen	X	Sets the script execution to the offset specified only if the stack is not true.
80	lineside	0	1	Hexen	X	See LineSide(0).
81	scriptwait	0	-1	Hexen	X	See ScriptWait(1).
82	scriptwaitdirect	1	0	Hexen	X	Same as scriptwait, uses constant parameters.
83	clearlinespecial	0	0	Hexen	X	See ClearLineSpecial(0).
84	casegoto	2	-1	Hexen	X	Sets the execution to the 2nd parameter if the stack is equal to the 1st.
85	beginprint	0	0	Hexen	X	Starts collecting information for the print or printbold functions.
86	endprint	0	0	Hexen	X	Finishes a print() call.
87	printstring	0	-1	Hexen	X	Adds the string referenced by the stack to the print.
88	printnumber	0	-1	Hexen	X	Adds the number referenced by the stack to the print.
89	printcharacter	0	-1	Hexen	X	Adds the character referenced by the stack to the print.
90	playercount	0	1	Hexen	X	See PlayerCount(0).
91	gametype	0	1	Hexen	X	See GameType(0).
92	gameskill	0	1	Hexen	X	See GameSkill(0).
93	timer	0	1	Hexen	X	See Timer(0).
94	sectorsound	0	-2	Hexen	X	See SectorSound(2).
95	ambientsound	0	-2	Hexen	X	See AmbientSound(2).
96	soundsequence	0	-1	Hexen	X	See SoundSequence(1).
97	setlinetexture	0	-4	Hexen	X	See SetLineTexture(4).
98	setlineblocking	0	-2	Hexen	X	See SetLineBlocking(2).[9]
99	setlinespecial	0	-7	Hexen	X	See SetLineSpecial(2,7).
100	thingsound	0	-3	Hexen	X	See ThingSound(3).
101	endprintbold	0	0	Hexen	X	Finishes the “bold” print statement. All players should receive this message.
102	activatorsound	0	-2	ZDoom		See ActivatorSound(2).
103	localambientsound	0	-2	ZDoom		See LocalAmbientSound(2).
104	setlinemonsterblocking	0	-2	ZDoom		See SetLineMonsterBlocking(2).
105	playerblueskull	0	1	Skulltag		Pushes -1 to the stack.
106	playerredskull	0	1	Skulltag		Pushes -1 to the stack.
107	playeryellowskull	0	1	Skulltag		Pushes -1 to the stack.
108	playermasterskull			Skulltag		Completely undefined at this time.
109	playerbluecard	0	1	Skulltag		Pushes -1 to the stack.
110	playerredcard	0	1	Skulltag		Pushes -1 to the stack.
111	playeryellowcard	0	1	Skulltag		Pushes -1 to the stack.
112	playermastercard			Skulltag		Completely undefined at this time.
113	playerblackskull			Skulltag		Completely undefined at this time.
114	playersilverskull			Skulltag		Completely undefined at this time.
115	playergoldskull			Skulltag		Completely undefined at this time.
116	playerblackcard			Skulltag		Completely undefined at this time.
117	playersilvercard			Skulltag		Completely undefined at this time.
118	playeronteam			Skulltag		Completely undefined at this time.
119	playerteam	0	1	Skulltag		See PlayerTeam(0).
120	playerhealth	0	1	Skulltag		See PlayerHealth(0).
121	playerarmorpoints	0	1	Skulltag		See PlayerArmorPoints(0).
122	playerfrags	0	1	Skulltag		See PlayerFrags(0).
123	playerexpert			Skulltag		Completely undefined at this time.
124	blueteamcount	0	1	Skulltag		See BlueCount(0).
125	redteamcount	0	1	Skulltag		See RedCount(0).
126	blueteamscore	0	1	Skulltag		See BlueScore(0).
127	redteamscore	0	1	Skulltag		See RedScore(0).
128	isoneflagctf	0	1	Skulltag		See IsOneFlagCTF(0).
129	getinvasionwave	0	1	Skulltag		See GetInvasionWave(0).
130	getinvasionstate	0	1	Skulltag		See GetInvasionState(0).
131	printname	0	-1	Skulltag		Adds the name of the player referenced by the number on the stack to the current print.
132	musicchange	0	-2	Skulltag		See Music_Change(2).
133	consolecommanddirect	3	0	Skulltag		Takes the specified command and executes it.[10] Last two parameters are unused.
134	consolecommand	0	-3	Skulltag		Same as consolecommanddirect, except it reads from the stack.
135	singleplayer	0	1	Skulltag		Pushes 1 to the stack if playing in single player otherwise pushes 0.
136	fixedmul	0	-1	ZDoom	X	Multiplies the last two fixed point numbers on the stack and pushes the result.
137	fixeddiv	0	-1	ZDoom	X	Divides the last two fixed point numbers on the stack and pushes the result.
138	setgravity	0	-1	ZDoom		See SetGravity(1).
139	setgravitydirect	1	0	ZDoom		Same as setgravity, uses constant parameters.
140	setaircontrol	0	-1	ZDoom		See SetAirControl(1).
141	setaircontroldirect	1	0	ZDoom		Same as setaircontrol, uses constant parameters.
142	clearinventory	0	0	ZDoom		See ClearInventory(0).
143	giveinventory	0	-2	ZDoom		See GiveInventory(2).
144	giveinventorydirect	2	0	ZDoom		Same as giveinventory, uses constant parameters.
145	takeinventory	0	-2	ZDoom		See TakeInventory(2).
146	takeinventorydirect	2	0	ZDoom		Same as takeinventory, uses constant parameters.
147	checkinventory	0	0	ZDoom		See CheckInventory(1).
148	checkinventorydirect	1	1	ZDoom		Same as checkinventory, uses constant parameters.
149	spawn	0	-5	ZDoom		See Spawn(4,6). Pushes 1 on success 0 on failure.
150	spawndirect	6	1	ZDoom		Same as spawn, uses constant parameters.
151	spawnspot	0	-3	ZDoom		See SpawnSpot(2,4). Pushes 1 on success 0 on failure.
152	spawnspotdirect	4	1	ZDoom		Same as spawnspot, uses constant parameters.
153	setmusic	0	-3	ZDoom		See SetMusic(1,3).
154	setmusicdirect	3	0	ZDoom		Same as setmusic, uses constant parameters.
155	localsetmusic	0	-3	ZDoom		See LocalSetMusic(1,3).
156	localsetmusicdirect	3	0	ZDoom		Same as localsetmusic, uses constant parameters.
157	printfixed	0	-1	ZDoom		Adds the fixed point number on the stack to the print.
158	printlocalized	0	-1	ZDoom		Adds the localized string referenced by the stack to the print command.
159	morehudmessage	0	0	ZDoom		Effectively ends the print portion of hudmessage. It does not print the message.
160	opthudmessage	0	0	ZDoom		Sets the position of hudmessage arguments in the stack to the current stack pointer. Finishing the parameter section of hudmessage. See hudmessage on the ZDoom wiki for detailed information on the parameters.
161	endhudmessage	0	x	ZDoom		Finishes an hudmessage command. Removing all parameters (terminated by opthudmessage) from the stack.
162	endhudmessagebold	0	x	ZDoom		Same as endhudmessage only prints the message to all players.
163	setstyle			ZDoom		Completely undefined at this time.
164	setstyledirect			ZDoom		Completely undefined at this time.
165	setfont	0	-1	ZDoom		See SetFont(1).
166	setfontdirect	1	0	ZDoom		Same as setfont, uses constant parameters.
167	pushbyte	1	0	ZDoom		Pushes a char onto the stack.
168	lspec1directb	2	0	ZDoom		Same as lspec1direct except all parameters are chars.
169	lspec2directb	3	0	ZDoom		Same as lspec2direct except all parameters are chars.
170	lspec3directb	4	0	ZDoom		Same as lspec3direct except all parameters are chars.
171	lspec4directb	5	0	ZDoom		Same as lspec4direct except all parameters are chars.
172	lspec5directb	6	0	ZDoom		Same as lspec5direct except all parameters are chars.
173	delaydirectb	1	0	ZDoom		Same as delaydirect except it takes a char.
174	randomdirectb	2	0	ZDoom		Same as randomdirect except all parameters are chars.
175	pushbytes	n+1	n	ZDoom		Pushes n chars to the stack where n is the first char.
176	push2bytes	2	2	ZDoom		Pushes 2 chars to the stack.
177	push3bytes	3	3	ZDoom		Pushes 3 chars to the stack.
178	push4bytes	4	4	ZDoom		Pushes 4 chars to the stack.
179	push5bytes	5	5	ZDoom		Pushes 5 chars to the stack.
180	setthingspecial	0	-7	ZDoom		See SetThingSpecial(2,7).
181	assignglobalvar	1	-1	ZDoom	X	Assigns the value on the stack to the specified global variable.
182	pushglobalvar	1	1	ZDoom	X	Pushes the value of the specified global variable onto the stack.
183	addglobalvar	1	-1	ZDoom	X	Adds the value of the stack to the specified global var.
184	subglobalvar	1	-1	ZDoom	X	Substracts the value of the stack from the specified global variable.
185	mulglobalvar	1	-1	ZDoom	X	Multiplies the global variable by the value on the stack.
186	divglobalvar	1	-1	ZDoom	X	Divides the global variable by the value on the stack. Errors on division by zero.
187	modglobalvar	1	-1	ZDoom	X	Does the modulus of the global variable with the value on the stack. Errors on modulus by zero.
188	incglobalvar	1	0	ZDoom	X	Increments the global variable by one.
189	decglobalvar	1	0	ZDoom	X	Decrements the global variable by one.
190	fadeto	0	-5	ZDoom		See FadeTo(5).
191	faderange	0	-9	ZDoom		See FadeRange(9).
192	cancelfade	0	0	ZDoom		See CancelFade(0).
193	playmovie	0	0	ZDoom		See PlayMovie(1).
194	setfloortrigger	0	-8	ZDoom		See SetFloorTrigger(3,8).
195	setceilingtrigger	0	-8	ZDoom		See SetCeilingTrigger(3,8).
196	getactorx	0	1	ZDoom		See GetActorX(1).
197	getactory	0	1	ZDoom		See GetActorY(1).
198	getactorz	0	1	ZDoom		See GetActorZ(1).
199	starttranslation	0	-1	ZDoom		Begins the translation definition for the translation specified on the stack. See CreateTranslation(2).
200	translationrange1	0	-4	ZDoom		Specifies a translation between palette indexes. Stack represents 1st:2nd=3rd:4th. See CreateTranslation(2).
201	translationrange2	0	-8	ZDoom		Specifies a translation from palette indexes to RGB values. Stack represents 1st:2nd=[3rd,4th,5th]:[6th,7th,8th]. See CreateTranslation(2).
202	endtranslation	0	0	ZDoom		Finishes a call to CreateTranslation(2).
203	call	1	1	ZDoom	X	Calls the function specified by index. Index will be a char in ACSe or a int otherwise.
204	calldiscard	1	0	ZDoom	X	Same as call, except the value returned will not be pushed to the stack. (Alternatively dropped.)
205	returnvoid	0	1/0	ZDoom	X	Returns from a function pushing 0 to the stack unless called by calldiscard.
206	returnval	0	1/0	ZDoom	X	Returns from a function keeping the top value of the stack unless called by calldiscard.
207	pushmaparray	1	0	ZDoom	X	Pushes the value of the specified map array at the index referenced by the stack.
208	assignmaparray	1	-2	ZDoom	X	Assigns the value of 1st stack item to the specified map array at the index referenced by the 2nd item.
209	addmaparray	1	-2	ZDoom	X	Adds the value of the 1st stack item to the specified map array at the index of the 2nd stack item.
210	submaparray	1	-2	ZDoom	X	Subtracts the value of the 1st stack item to the specified map array at the index of the 2nd stack item.
211	mulmaparray	1	-2	ZDoom	X	Multiplies the specified map array's index referenced by the 2nd item on the stack by the 1st.
212	divmaparray	1	-2	ZDoom	X	Divides the specified map array's index referenced by the 2nd item on the stack by the 1st. Errors on division by zero.
213	modmaparray	1	-2	ZDoom	X	Performs the modulus of the specified map array's index referenced by the 2nd item on the stack by the 1st item on the stack. Errors on modulus by zero.
214	incmaparray	1	-1	ZDoom	X	Increments the specified map array at the index referenced by the stack by one.
215	decmaparray	1	-1	ZDoom	X	Decrements the specified map array at the index referenced by the stack by one.
216	dup	0	1	ZDoom		Pushes the value of the stack to the stack.
217	swap	0	0	ZDoom		Switches the last two values on the stack.
218	writetoini			ZDoom		Completely undefined at this time.
219	getfromini			ZDoom		Completely undefined at this time.
220	sin	0	0	ZDoom		See Sin(1).
221	cos	0	0	ZDoom		See Cos(1).
222	vectorangle	0	-1	ZDoom		See VectorAngle(2).
223	checkweapon	0	0	ZDoom		See CheckWeapon(1).
224	setweapon	0	0	ZDoom		See SetWeapon(1).
225	tagstring	0	0	ZDoom	X	Puts the id of the library into upper 16-bits of the stack.
226	pushworldarray	1	0	ZDoom	X	Pushes the value of the specified world array at the index referenced by the stack.
227	assignworldarray	1	-2	ZDoom	X	Assigns the value of 1st stack item to the specified world array at the index referenced by the 2nd item.
228	addworldarray	1	-2	ZDoom	X	Adds the value of the 1st stack item to the specified world array at the index of the 2nd stack item.
229	subworldarray	1	-2	ZDoom	X	Subtracts the value of the 1st stack item to the specified world array at the index of the 2nd stack item.
230	mulworldarray	1	-2	ZDoom	X	Multiplies the specified world array's index referenced by the 2nd item on the stack by the 1st.
231	divworldarray	1	-2	ZDoom	X	Divides the specified world array's index referenced by the 2nd item on the stack by the 1st. Errors on division by zero.
232	modworldarray	1	-2	ZDoom	X	Performs the modulus of the specified world array's index referenced by the 2nd item on the stack by the 1st item on the stack. Errors on modulus by zero.
233	incworldarray	1	-1	ZDoom	X	Increments the specified world array at the index referenced by the stack by one.
234	decworldarray	1	-1	ZDoom	X	Decrements the specified world array at the index referenced by the stack by one.
235	pushglobalarray	1	0	ZDoom	X	Pushes the value of the specified global array at the index referenced by the stack.
236	assignglobalarray	1	-2	ZDoom	X	Assigns the value of 1st stack item to the specified global array at the index referenced by the 2nd item.
237	addglobalarray	1	-2	ZDoom	X	Adds the value of the 1st stack item to the specified global array at the index of the 2nd stack item.
238	subglobalarray	1	-2	ZDoom	X	Subtracts the value of the 1st stack item to the specified global array at the index of the 2nd stack item.
239	mulglobalarray	1	-2	ZDoom	X	Multiplies the specified global array's index referenced by the 2nd item on the stack by the 1st.
240	divglobalarray	1	-2	ZDoom	X	Divides the specified global array's index referenced by the 2nd item on the stack by the 1st. Errors on division by zero.
241	modglobalarray	1	-2	ZDoom	X	Performs the modulus of the specified global array's index referenced by the 2nd item on the stack by the 1st item on the stack. Errors on modulus by zero.
242	incglobalarray	1	-1	ZDoom	X	Increments the specified global array at the index referenced by the stack by one.
243	decglobalarray	1	-1	ZDoom	X	Decrements the specified global array at the index referenced by the stack by one.
244	setmarineweapon	0	-2	ZDoom		See SetMarineWeapon(2).
245	setactorproperty	0	-3	ZDoom		See SetActorProperty(3).
246	getactorproperty	0	-1	ZDoom		See GetActorProperty(2).
247	playernumber	0	1	ZDoom		See PlayerNumber(0).
248	activatortid	0	1	ZDoom		See ActivatorTID(0).
249	setmarinesprite	0	-2	ZDoom		See SetMarineSprite(2).
250	getscreenwidth	0	1	ZDoom		See GetScreenWidth(0).
251	getscreenheight	0	1	ZDoom		See GetScreenHeight(0).
252	thingprojectile2	0	-7	ZDoom		See Thing_Projectile2(7).
253	strlen	0	0	ZDoom	X	See StrLen(1).
254	sethudsize	0	-3	ZDoom		See SetHudSize(3).
255	getcvar	0	0	ZDoom		See GetCVar(1).
256	casegotosorted	2n+1	-1/0	ZDoom	X	First ensure that your script data pointer is 4 byte aligned by padding after the pcode. The first int indicates the number of cases. The cases should be sorted in such a way that a binary search may be performed. For each case in the table there is a value-address int pair. / The stack is only popped if a match is found.
257	setresultvalue	0	-1	ZDoom	X	Sets the result of the script to the stack.
258	getlinerowoffset	0	1	ZDoom		See GetLineRowOffset(0).
259	getactorfloorz	0	0	ZDoom		See GetActorFloorZ(1).
260	getactorangle	0	0	ZDoom		See GetActorAngle(1).
261	getsectorfloorz	0	-2	ZDoom		See GetSectorFloorZ(3).
262	getsectorceilingz	0	-2	ZDoom		See GetSectorCeilingZ(3).
263	lspec5result	1	-4	ZDoom	X	Same as lspec5 except the result of the special is pushed onto the stack.
264	getsigilpieces	0	1	ZDoom		See GetSigilPieces(0).
265	getlevelinfo	0	0	ZDoom		See GetLevelInfo(1).
266	changesky	0	-2	ZDoom		See ChangeSky(2).
267	playeringame	0	0	ZDoom		See PlayerInGame(1).
268	playerisbot	0	0	ZDoom		See PlayerIsBot(1).
269	setcameratotexture	0	-3	ZDoom		See SetCameraToTexture(3).
270	endlog	0	0	ZDoom		Ends a log call.
271	getammocapacity	0	0	ZDoom		See GetAmmoCapacity(1).
272	setammocapacity	0	-2	ZDoom		See SetAmmoCapacity(2).
273	printmapchararray	0	-2	ZDoom		Adds the string represented by the character array in the map array specified by the 1st stack item at the offset in the 2nd stack item.
274	printworldchararray	0	-2	ZDoom		Adds the string represented by the character array in the world array specified by the 1st stack item at the offset in the 2nd stack item.
275	printglobalchararray	0	-2	ZDoom		Adds the string represented by the character array in the global array specified by the 1st stack item at the offset in the 2nd stack item.
276	setactorangle	0	-2	ZDoom		See SetActorAngle(2).
277	grabinput			ZDoom		Completely undefined at this time.
278	setmousepointer			ZDoom		Completely undefined at this time.
279	movemousepointer			ZDoom		Completely undefined at this time.
280	spawnprojectile	0	-7	ZDoom		See SpawnProjectile(7).
281	getsectorlightlevel	0	0	ZDoom		See GetSectorLightLevel(1).
282	getactorceilingz	0	0	ZDoom		See GetActorCeilingZ(1).
283	setactorposition	0	-4	ZDoom		See SetActorPosition(5).
284	clearactorinventory	0	-1	ZDoom		See ClearActorInventory(1).
285	giveactorinventory	0	-3	ZDoom		See GiveActorInventory(3).
286	takeactorinventory	0	-3	ZDoom		See TakeActorInventory(3).
287	checkactorinventory	0	-1	ZDoom		See CheckActorInventory(2).
288	thingcountname	0	-1	ZDoom		See ThingCountName(2).
289	spawnspotfacing	0	-2	ZDoom		See SpawnSpotFacing(3).
290	playerclass	0	0	ZDoom		See PlayerClass(1).
291	andscriptvar	1	-1	ZDoom	X	Performs the bitwise and operation with the specified local variable and the stack.
292	andmapvar	1	-1	ZDoom	X	Performs the bitwise and operation with the specified map variable and the stack.
293	andworldvar	1	-1	ZDoom	X	Performs the bitwise and operation with the specified world variable and the stack.
294	andglobalvar	1	-1	ZDoom	X	Performs the bitwise and operation with the specified global variable and the stack.
295	andmaparray	1	-2	ZDoom	X	Performs the bitwise and operation with the specified map array at the index of the 2nd stack item and the 1st stack item.
296	andworldarray	1	-2	ZDoom	X	Performs the bitwise and operation with the specified world array at the index of the 2nd stack item and the 1st stack item.
297	andglobalarray	1	-2	ZDoom	X	Performs the bitwise and operation with the specified global array at the index of the 2nd stack item and the 1st stack item.
298	eorscriptvar	1	-1	ZDoom	X	Performs the bitwise exclusive or operation with the specified local variable and the stack.
299	eormapvar	1	-1	ZDoom	X	Performs the bitwise exclusive or operation with the specified map variable and the stack.
300	eorworldvar	1	-1	ZDoom	X	Performs the bitwise exclusive or operation with the specified world variable and the stack.
301	eorglobalvar	1	-1	ZDoom	X	Performs the bitwise exclusive or operation with the specified global variable and the stack.
302	eormaparray	1	-2	ZDoom	X	Performs the bitwise excluse or operation with the specified map array at the index of the 2nd stack item and the 1st stack item.
303	eorworldarray	1	-2	ZDoom	X	Performs the bitwise excluse or operation with the specified world array at the index of the 2nd stack item and the 1st stack item.
304	eorglobalarray	1	-2	ZDoom	X	Performs the bitwise excluse or operation with the specified global array at the index of the 2nd stack item and the 1st stack item.
305	orscriptvar	1	-1	ZDoom	X	Performs the bitwise or operation with the specified local variable and the stack.
306	ormapvar	1	-1	ZDoom	X	Performs the bitwise or operation with the specified map variable and the stack.
307	orworldvar	1	-1	ZDoom	X	Performs the bitwise or operation with the specified world variable and the stack.
308	orglobalvar	1	-1	ZDoom	X	Performs the bitwise or operation with the specified global variable and the stack.
309	ormaparray	1	-2	ZDoom	X	Performs the bitwise or operation with the specified map array at the index of the 2nd stack item and the 1st stack item.
310	orworldarray	1	-2	ZDoom	X	Performs the bitwise or operation with the specified world array at the index of the 2nd stack item and the 1st stack item.
311	orglobalarray	1	-2	ZDoom	X	Performs the bitwise or operation with the specified global array at the index of the 2nd stack item and the 1st stack item.
312	lsscriptvar	1	-1	ZDoom	X	Left shifts the specified local variable by the stack.
313	lsmapvar	1	-1	ZDoom	X	Left shifts the specified map variable by the stack.
314	lsworldvar	1	-1	ZDoom	X	Left shifts the specified world variable by the stack.
315	lsglobalvar	1	-1	ZDoom	X	Left shifts the specified global variable by the stack.
316	lsmaparray	1	-2	ZDoom	X	Left shifts the specified map array at the index referenced by the 2nd stack item by the 1st item.
317	lsworldarray	1	-2	ZDoom	X	Left shifts the specified world array at the index referenced by the 2nd stack item by the 1st item.
318	lsglobalarray	1	-2	ZDoom	X	Left shifts the specified global array at the index referenced by the 2nd stack item by the 1st item.
319	rsscriptvar	1	-1	ZDoom	X	Right shifts the specified local variable by the stack.
320	rsmapvar	1	-1	ZDoom	X	Right shifts the specified map variable by the stack.
321	rsworldvar	1	-1	ZDoom	X	Right shifts the specified world variable by the stack.
322	rsglobalvar	1	-1	ZDoom	X	Right shifts the specified global variable by the stack.
323	rsmaparray	1	-2	ZDoom	X	Right shifts the specified map array at the index referenced by the 2nd stack item by the 1st item.
324	rsworldarray	1	-2	ZDoom	X	Right shifts the specified local array at the index referenced by the 2nd stack item by the 1st item.
325	rsglobalarray	1	-2	ZDoom	X	Right shifts the specified global array at the index referenced by the 2nd stack item by the 1st item.
326	getplayerinfo	0	-1	ZDoom		See GetPlayerInfo(2).
327	changelevel	0	-4	ZDoom		See ChangeLevel(3,4).
328	sectordamage	0	-5	ZDoom		See SectorDamage(5).
329	replacetextures	0	-3	ZDoom		See ReplaceTextures(2,3).
330	negatebinary	0	0	ZDoom	X	Performs a binary negation on the stack.
331	getactorpitch	0	0	ZDoom		See GetActorPitch(1).
332	setactorpitch	0	-2	ZDoom		See SetActorPitch(2).
333	printbind	0	-1	ZDoom		Adds the name of the key in which the action referenced by the stack is bound to the print.
334	setactorstate	0	-2	ZDoom		See SetActorState(2,3).
335	thingdamage2	0	-2	ZDoom		See Thing_Damage2(3).
336	useinventory	0	0	ZDoom		See UseInventory(1).
337	useactorinventory	0	-1	ZDoom		See UseActorInventory(2).
338	checkactorceilingtexture	0	-1	ZDoom		See CheckActorCeilingTexture(2).
339	checkactorfloortexture	0	-1	ZDoom		See CheckActorFloorTexture(2).
340	getactorlightlevel	0	0	ZDoom		See GetActorLightLevel(1).
341	setmugshotstate	0	-1	ZDoom		See SetMugShotState(1).
342	thingcountsector	0	-2	ZDoom		See ThingCountSector(3).
343	thingcountnamesector	0	-2	ZDoom		See ThingCountNameSector(3).
344	checkplayercamera	0	0	ZDoom		See CheckPlayerCamera(1).
345	morphactor	0	-6	ZDoom		See MorphActor(1,7).
346	unmorphactor	0	-1	ZDoom		See UnMorphActor(1,2).
347	getplayerinput	0	-1	ZDoom		See GetPlayerInput(2).
348	classifyactor	0	0	ZDoom		See ClassifyActor(1).
349	printbinary	0	-1	ZDoom		Adds the binary number to the print.
350	printhex	0	-1	ZDoom		Adds the hexadecimal number to the print.
351	callfunc	2	-n+1	ZDoom	X	Calls an alternative type of built in function. The first char following the PCode is the number of arguments. The next short is the function index (see below). After all of the arguments are removed from the stack, the return value is pushed to the stack. If this is used ourside of ACSe the first two parameters are also ints.
352	savestring	0	1	ZDoom		Creates a temporary string in the string table based on the print string. Pushes the new strings index.
353	printmapchrange	0	-4	ZDoom		Same as printmapchararray except two stack values are added to the beginning, one for length and the other for an offset. The offset from printmapchararray will be added to this offset.
354	printworldchrange	0	-4	ZDoom		See printmapchrange.
355	printglobalchrange	0	-4	ZDoom		See printmapchrange.
356	strcpytomapchrange	0	-5	ZDoom		Copies a string to a character array. First stack argument is the offset of the destination array. Second is the id of the array. Third is the checked offset of the destination (first will be added to this value). Fourth is the length of the destination buffer. Fifth is the string which is to be copied, and sixth is the offset within the string. True is pushed to the stack if the copy is sucessful.
357	strcpytoworldchrange	0	-5	ZDoom		See strcpytomapchrange.
358	strcpytoglobalchrange	0	-5	ZDoom		See strcpytomapchrange.
359	pushfunction	1	1	Eternity		Pushes a pointer to the module's function onto the stack. In ACSe the argument should be a char.
360	callstack	0	0	Eternity		Calls the function pointed by the stack argument and pushes the result to the stack.
361	scriptwaitnamed	0	-1	ZDoom		See NamedScriptWait(1).
362	translationrange3	0	-8	ZDoom		Specifies a translation from palette indexes by desaturation across RGB values. Stack represents 1st:2nd=%[3rd,4th,5th]:[6th,7th,8th]. See CreateTranslation(2).
[8] In ZDoom this is handled identically to the PCode setresultvalue.
[9] In Hexen it may be assumed that the second argument to this function is a boolean, however other ports have extended this to include multiple flags.
[10] It is worth noting here that consolecommand can be a serious security issue. As such I would advise against implementing it.

## Additional Functions
The callfunc PCode references a table of functions. These functions are handled similar to the normal built in functions, however they are more flexible (argument count is not a constant for example). The PCode always pushes a return value onto the stack so it must be dropped if it is to be ignored. Continue to refer to the ZDoom wiki's built in ACS function documentation for details on their exact operations.
#	Function	Args	Ret	Req
1	GetLineUDMFInt	2	int
2	GetLineUDMFFixed	2	fixed
3	GetThingUDMFInt	2	int
4	GetThingUDMFFixed	2	fixed
5	GetSectorUDMFInt	2	int
6	GetSectorUDMFFixed	2	fixed
7	GetSideUDMFInt	3	int
8	GetSideUDMFFixed	3	fixed
9	GetActorVelX	1	int
10	GetActorVelY	1	int
11	GetActorVelZ	1	int
12	SetActivator	1	bool
13	SetActivatorToTarget	1	bool
14	GetActorViewHeight	1	int
15	GetChar	2	char	X
16	GetAirSupply	1	int
17	SetAirSupply	2	bool
18	SetSkyScrollSpeed	2	bool
19	GetArmorType	2	int
20	SpawnSpotForced	4	bool
21	SpawnSpotFacingForced	3	bool
22	CheckActorProperty	3	bool
23	SetActorVelocity	6	void
24	SetUserVariable	3	int
25	GetUserVariable	2	int
26	Radius_Quake2	6	void
27	CheckActorClass	2	bool
28	SetUserArray	4	int
29	GetUserArray	3	int
30	SoundSequenceOnActor	2	void
31	SoundSequenceOnSector	3	void
32	SoundSequenceOnPolyobj	2	void
33	GetPolyobjX	1	int
34	GetPolyobjY	1	int
35	CheckSight	3	bool
36	SpawnForced	6	int
37	AnnouncerSound	1	void
38	SetPointer	4	bool
39	ACS_NamedExecute	5	bool
40	ACS_NamedSuspend	5	bool
41	ACS_NamedTerminate	5	bool
42	ACS_NamedLockedExecute	5	bool
43	ACS_NamedLockedExecuteDoor	5	bool
44	ACS_NamedExecuteWithResult	5	int
45	ACS_NamedExecuteAlways	5	bool
46	UniqueTID	2	bool
47	IsTIDUsed	1	bool
48	Sqrt	1	int
49	FixedSqrt	1	fixed
50	VectorLength	2	int
51	SetHUDClipRect	5	void
52	SetHUDWrapWidth	1	void
100	ResetMap	0	bool
101	PlayerIsSpectator	1	bool
102	ConsolePlayerNumber	0	int
103	GetTeamProperty	2	int
19620	GetTeamScore	1	int
19621	SetTeamScore	2	void